## Slide 1
R0
C0
Iinput
Here’s our equivalent circuit for a cell membrane with an (open) channel – part of the LIF model
To gain biophysical intuition, let’s examine how this circuit behaves as we inject charge ...

## Slide 2
No charge on capacitor
Case 1: Set C0 = 1 farad, R0 = 1 ohm
Time: t = 0 s
R0
C0
Not yet injecting current

## Slide 3
R0
C0
Iinput
Case 1: Set C0 = 1 farad, R0 = 1 ohm, and Iinput = 1 charge / sec = 1 amp
+
“What is the voltage?”
Q = C V
V = 0 coloumb / 1 farad
V = 0
iR = V/R =
0 amp
iC = Iinput – iR =
1 amp
Time: t = 1 s
“Where do I go?”
All charge goes to capacitor

## Slide 4
R0
C0
Iinput
Case 1: Set C0 = 1 farad, R0 = 1 ohm, and Iinput = 1 charge / sec = 1 amp
+
“What is the voltage?”
Q = C V
V = 1 coloumb / 1 farad
V = 1 volt
iR = V/R =
1 amp
iC = Iinput – iR =
0 amp
Time: t = 2 s
“Where do I go?”
+
All charge leaves through resistor.
We’ve reached equilibrium
  V* = 1 volt, t = 1 s

## Slide 5
Case 2: Set C0 = 2 farad, R0 = 1 ohm, and Iinput = 1 charge / sec = 1 amp
Double the capacitance!
No charge on capacitor
Time: t = 0 s
R0
C0
Not yet injecting current

## Slide 6
R0
C0
Iinput
Case 2: Set C0 = 2 farad, R0 = 1 ohm, and Iinput = 1 charge / sec = 1 amp
+
“What is the voltage?”
Q = C V
V = 0 coloumb / 1 farad
V = 0
iR = V/R =
0 amp
iC = Iinput – iR =
1 amp
Time: t = 1 s
“Where do I go?”
1st charge to capacitor

## Slide 7
R0
C0
Iinput
Case 2: Set C0 = 2 farad, R0 = 1 ohm, and Iinput = 1 charge / sec = 1 amp
+
“What is the voltage?”
Q = C V
V = 1 coloumb / 2 farad
V = 0.5 volt
iR = V/R =
0.5 amp
iC = Iinput – iR =
0.5 amp
Time: t = 2 s
“Where do I go?”
+
½ to capacitor, ½ to resistor

## Slide 8
R0
C0
Iinput
Case 2: Set C0 = 2 farad, R0 = 1 ohm, and Iinput = 1 charge / sec = 1 amp
+
“What is the voltage?”
Q = C V
V = 1.5 coloumb / 2 farad
V = 0.75 volt
iR = V/R =
0.75 amp
iC = Iinput – iR =
0.25 amp
Time: t = 3 s
“Where do I go?”
+
¼ to capacitor, ¾ to resistor
+

## Slide 9
R0
C0
Iinput
Case 2: Set C0 = 2 farad, R0 = 1 ohm, and Iinput = 1 charge / sec = 1 amp
+
“What is the voltage?”
Q = C V
V = 1.75 coloumb / 2 farad
V = 0.875 volt
iR = V/R =
0.875 amp
iC = Iinput – iR =
0.125 amp
Time: t = 4 s
“Where do I go?”
+
7/8 to capacitor, 1/8 to resistor
+
+

## Slide 10
R0
C0
Iinput
Case 2: Set C0 = 2 farad, R0 = 1 ohm, and Iinput = 1 charge / sec = 1 amp
“What is the voltage?”
Q = C V
V = 2 coloumb / 2 farad
V = 1 volt
iR = V/R =
1 amp
iC = Iinput – iR =
0 amp
Time: t = goes on
“Where do I go?”
+
Eventually (at equilibrium):
2 charges on capacitor
V* = 1 volt
t = longer time ... (> 1 s)
+
+

## Slide 11
Case 2: Set C0 = 2 farad, R0 = 1 ohm, and Iinput = 1 charge / sec = 1 amp
So, double the capacitance:
double charge on capacitor
same target voltage (1 volt)
longer time to get there (bigger time constant)

## Slide 12
Case 3: Set C0 = 1 farad, R0 = 2 ohm, and Iinput = 1 charge / sec = 1 amp
Double the resistance!
No charge on capacitor
Time: t = 0 s
R0
C0
Not yet injecting current

## Slide 13
R0
C0
Iinput
+
“What is the voltage?”
Q = C V
V = 0 coloumb / 1 farad
V = 0
iR = V/R =
0 amp
iC = Iinput – iR =
1 amp
Time: t = 1 s
“Where do I go?”
1st charge to capacitor
Case 3: Set C0 = 1 farad, R0 = 2 ohm, and Iinput = 1 charge / sec = 1 amp

## Slide 14
R0
C0
Iinput
+
“What is the voltage?”
Q = C V
V = 1 coloumb / 1 farad
V = 1 volt
iR = V/R =
= 0.5 amp
iC = Iinput – iR =
0.5 amp
Time: t = 2 s
“Where do I go?”
+
½ to capacitor, ½ to resistor
Case 3: Set C0 = 1 farad, R0 = 2 ohm, and Iinput = 1 charge / sec = 1 amp
1 volt / 2 ohm

## Slide 15
R0
C0
Iinput
+
“What is the voltage?”
Q = C V
V = 1.5 coloumb / 1 farad
V = 1.5 volt
iR = V/R =
iC = Iinput – iR =
0.25 amp
Time: t = 3 s
“Where do I go?”
+
¼ to capacitor, ¾ to resistor
+
Case 3: Set C0 = 1 farad, R0 = 2 ohm, and Iinput = 1 charge / sec = 1 amp
= 0.75 amp
1.5 volt / 2 ohm

## Slide 16
R0
C0
Iinput
+
“What is the voltage?”
Q = C V
V = 1.75 coloumb / 1 farad
V = 1.75 volt
iR = V/R =
iC = Iinput – iR =
0.125 amp
Time: t = 4 s
“Where do I go?”
+
7/8 to capacitor, 1/8 to resistor
+
+
Case 3: Set C0 = 1 farad, R0 = 2 ohm, and Iinput = 1 charge / sec = 1 amp
= 0.875 amp
1.75 volt / 2 ohm

## Slide 17
R0
C0
Iinput
“What is the voltage?”
Q = C V
V = 2 coloumb / 1 farad
V = 2 volt
iR = V/R =
1 amp
iC = Iinput – iR =
0 amp
Time: t = goes on
“Where do I go?”
+
Eventually (at equilibrium):
2 charges on capacitor
V* = 2 volt
t = longer time ... (> 1 s)
+
Case 3: Set C0 = 1 farad, R0 = 2 ohm, and Iinput = 1 charge / sec = 1 amp
+

## Slide 18
So, double the resistance:
double charge on capacitor
double target voltage (2 volt)
longer time to get there (bigger time constant)
Case 3: Set C0 = 1 farad, R0 = 2 ohm, and Iinput = 1 charge / sec = 1 amp

## Slide 19
Summary
double the resistance
double the capacitance
t = R C
 doubles
Cell higher capacity to hold charge
Cell same capacity to hold charge
So takes longer to charge it up.
V* = I R
 doubles
Cell higher target voltage
need enough charge here,
to make V big enough ...
... to force future charges
out through the (smaller) channel
doubles
V* fixed
doubles
V* doubles